midi / split / Thankyou for buying this kit! The information on this slip is the bare minimum you will need to build the project. You will find expanded information, including step by step build instructions with photographs, at / https://github.com/hotchk155/MIDI-Splitter/wiki / The component designators used on the PCB are listed below / R1, R2, R3, R4, R5, R6, R7, R8, R9, R10, R11, R12, R21 - 220 Ohm (red-red-brown code) resistor. R1 through R12 are fitted “standing up” on the board and I recommend soldering them after the other components. / R13,R16,R17 – 1 kOhm (brown-black-red code) resistor / R14,R15 – 1.5 kOhm (black-green-red code) resistor / C1 - 100nF ceramic (104 code) capacitor / The following components must be soldered the correct way around. Use the markings on the PCB for orientation or check the above link if in doubt. All are soldered to the top side of the PCB. / Q1 - 2N3906 general purpose PNP transistor / C3 – 4.7uF electrolytic capacitor / D1 - 1N4148 small signal diode / IC1 - 4050 hex non-inverting buffer (DIL16) with socket / IC2 - 6N138 Opto Coupler (DIL8) with socket / CN2 - Mini USB connector / Solder the IC sockets before fitting ICs. Check orientation of pin 1 notch/dimple with markings on PCB) / The following LEDs are fitted close to the mini USB socket / POWER (left of socket) - Standard brightness RED LED / ACTIVITY (right of socket) - High brightness BLUE LED / Solder the seven MIDI sockets last and make sure that they are fitted flush to the board. This is important to ensure the solder joints to the sockets do not get strained and damaged in use. / Use the machine screws, nylon standoffs and nuts to attach the acrylic base plate to the PCB. Attach the self-adhesive rubber feet to the userside of the base plate. / I hope you find this kit useful. If you have any problems please contact me at the following email sixtyfourpixels@gmail.com or via the site where you ordered the kit / midi split is an open hardware project. All input and feedback is welcome / Cheers, / Jason Hotchk155	midi / split / Thankyou for buying this kit! The information on this slip is the bare minimum you will need to build the project. You will find expanded information, including step by step build instructions with photographs, at / https://github.com/hotchk155/MIDI-Splitter/wiki / The component designators used on the PCB are listed below / R1, R2, R3, R4, R5, R6, R7, R8, R9, R10, R11, R12, R21 - 220 Ohm (red-red-brown code) resistor. R1 through R12 are fitted “standing up” on the board and I recommend soldering them after the other components. / R13,R16,R17 – 1 kOhm (brown-black-red code) resistor / R14,R15 – 1.5 kOhm (black-green-red code) resistor / C1 - 100nF ceramic (104 code) capacitor / The following components must be soldered the correct way around. Use the markings on the PCB for orientation or check the above link if in doubt. All are soldered to the top side of the PCB. / Q1 - 2N3906 general purpose PNP transistor / C3 – 4.7uF electrolytic capacitor / D1 - 1N4148 small signal diode / IC1 - 4050 hex non-inverting buffer (DIL16) with socket / IC2 - 6N138 Opto Coupler (DIL8) with socket / CN2 - Mini USB connector / Solder the IC sockets before fitting ICs. Check orientation of pin 1 notch/dimple with markings on PCB) / The following LEDs are fitted close to the mini USB socket / POWER (left of socket) - Standard brightness RED LED / ACTIVITY (right of socket) - High brightness BLUE LED / Solder the seven MIDI sockets last and make sure that they are fitted flush to the board. This is important to ensure the solder joints to the sockets do not get strained and damaged in use. / Use the machine screws, nylon standoffs and nuts to attach the acrylic base plate to the PCB. Attach the self-adhesive rubber feet to the userside of the base plate. / I hope you find this kit useful. If you have any problems please contact me at the following email sixtyfourpixels@gmail.com or via the site where you ordered the kit / midi split is an open hardware project. All input and feedback is welcome / Cheers, / Jason Hotchk155